Modules of the project
Interaction with player
Physics engine structure
Unit structure
Collision matching
Collision events
GUI
Our game project

---
Modules of the project
Each 1/n seconds
Physics engine
Game
GUI
State before matching
Current state
Game objects
State after matching

---
Interaction with player
Game
Reads state of needed keys in each frame
Keys states (is pressed now or not) shared buffer
0
1
If key is pushed set key state to 1
If key is pulled set key state to 0
GUI

---
Physics engine structure
World represents engine functionality.

---
Unit structure
uver
Size and position of unit can be described by two points: left bottom (x1,y1) ant top right (x2,y2).
For describe current state of the unit in the world it’s enough to have a two current speed vectors: vertical and horizontal. Measure of speed in our game context is points per frame. Each frame = n seconds. Also it is speed given by gravitation, and it always force unit.
If unit is alone with no other units, it has only vertical gravitation speed, witch make unit move down.
If two blocks bumped, block with lower priority takes speed of block with higher priority. So each unit should have priority. Units of ground and walls normally have the largest priority.
(x2,y2)
Unit
uhor
(x1,y1)
ug
[u csup{ rightarrow } ]= {points csup{ rightarrow }} over {frame}
(x2,y2)
Unit
(x1,y1)
ug

---
Collision matching
collision
1.
2.
(x2+uh,y2)
(x2,y2)
Unit2
Unit
Unit2
Unit
(x1,y1)
(x1,y1)
collision
3.
(x2+uh,y2)
Try move unit2 according its
speed. If it resolve collision, match collisions for y
moving. For unit and mark unit2 as moved. Else
find point of touch and resolve collision by changing
of positions and speeds.
Unit2
Unit
(x1,y1)

---
Collision matching
- There are three sets of objects: static, mobs and players.
- Collisions are matching only between different sets.
Static
players
mobs

---
Collision events
Each collision cause changing of speeds and positions of units